## Slide 1: Improving predictions of coastal flooding via sub-mesh corrections
Johnathan Woodruff1, J.C. Dietrich1
A. Kennedy2, D. Wirasaet2, D. Bolster2, Z. Silver2, R. Kolar3 1North Carolina State University – Raleigh, NC, 2University of Notre Dame – South Bend, IN, 3University of Oklahoma – Norman, OK

## Slide 2: Introduction
High resolution is computationally costly
  Hinders the speed of ADCIRC runs
  Delays the forecast predictions
This study aims to increase the accuracy and efficiency of ADCIRC by:
  Adding sub-mesh correction factors to the governing equations
  Running on coarsened meshes

## Slide 3
Caernarvon Marsh, LA
1.
2.
3.
NOMAD mesh v1e MSL (HSOFS)
This mesh is used in real-time forecasting by NOAA and the ADCIRC Prediction System (APS).
High resolution bathymetry surrounding Delacroix, LA
Interpolated bathymetry of the mesh

## Slide 4: Sub-mesh Features
Sub-mesh features:
  Hydraulic features that influence flow
  Exist below the resolution of the mesh
  Include: small scale channels, ponds, marsh grasses, and roadways
50-100 m
10 m
Pond
Tidal Channel
Marsh Grass

## Slide 5: Theory
The primitive shallow water equations were first averaged using techniques outlined in Kennedy et al. 2019.
These averaged primitive equations were then transformed into the GWCE and conservative momentum equations ADCIRC uses.

## Slide 6: Averaged Variables Theory
To obtain the averaged variables we integrate inside each element.
A given dummy variable would be averaged as follows:
Where:

## Slide 7: GWCE Conversion
Where:
is the wet area fraction
Subscripts and mean the variable was averaged over the wet area or whole area respectively

## Slide 8: GWCE Conversion

## Slide 9: Sub-mesh calculations
Sub-mesh calculations are performed using a high resolution digital elevation model (DEM) underlying a ADCIRC mesh of coarser resolution.
Sub-mesh correction factors such as , , and are found by integrating the sub-areas within each element.
Sub-mesh quantities are pre-computed and read into ADCIRC.
ELEMENT 1
WET
PARTIALLY WET
DRY
ELEMENT 2
ELEMENT 3
NODE 2
NODE 3

## Slide 10: Sub-mesh calculations
Within the elemental loops of the GWCE and Momentum codes averaged variables are looked up based on water surface elevation at each vertex.
Averaged variables are also stored in vertex arrays to be used in wetting and drying and the nodal loops of the momentum code.
ELEMENT 1
WET
PARTIALLY WET
DRY
ELEMENT 2
ELEMENT 3
NODE 2
NODE 3

## Slide 11: Sub-mesh in 2D
= WET
= PARTIALLY WET
= DRY
In 2D the elements are split up into 3 sub-areas.
Sub-mesh calculations are performed based on the DEM lying beneath the mesh for each sub-area within the element.

## Slide 12: Sub-mesh in 2D
DEM Res
Divide element into 3 sub-areas based on the halfway points between vertices.
Divide each sub-area into 2 triangles
Refine each triangle into many smaller triangles that are roughly the same resolution as the sub-mesh
Apply DEM data to the smaller triangles
Average sub-mesh variables over each sub-area

## Slide 13: Wetting and Drying
REALITY
TRADITIONAL ADCIRC
DRY
DRY
WET
WET
DRY
PARTIALLY
WET
DRY
WET
SUB-MESH ADCIRC

## Slide 14: Wetting and Drying Algorithm
A totally new wetting and drying algorithm was used to replace the existing.
The wet/dry state of each vertex is determined based on the wet area surrounding the vertex.
Elemental wet/dry state is determined by the average wet area within each element.

## Slide 15: Wetting and Drying Algorithm
BEGIN Wetting and Drying
ADJUST
of DRY vertices to the of the neighboring WET vertices
COMPUTE averaged variables , ,
EVALUATE wet/dry state
END Wetting and Drying

## Slide 16: Discretization
The discretization of the governing equations mimics the Conservative Version 1 discretization.
Conservative Version 1 assumes the un-differentiated terms are elementally averaged and uses a linear expansion in space for the conservative flux terms.

## Slide 17: Results
Sub-mesh ADCIRC was run on a coarsened mesh to demonstrate its ability to accurately predict water surface elevations.
Traditional ADCIRC was run on both a coarsened and high resolution mesh as a baseline to compare sub-mesh results.

## Slide 18: Model Setup
DT = 1 second
= 0.005
FFACTOR = 0.0025
ESLM = 2.0
No ramp
1 day runtime
Sub-mesh
2 m diurnal tidal signal was used to force the model
Kolar-Gray Lat. Stress GWCE
Cons. Form 1 Advec. GWCE
INTBP Velocity Based Lat. Stress
Cons. Form 1 Advec. Momentum
Corrected Area Integration Mom.
Implicit Formulation
1
2
1
2
1
1
IM CODE

## Slide 19
High resolution (10 m) DEM featuring a 250 m wide winding channel was used to calculate the sub-mesh variables.
12000 m
12000 m
250 m

## Slide 20
High resolution mesh was created using this DEM.
This mesh resolves the small channel.
Vertices: 6420 Elements: 12742
12000 m
12000 m
500 m

## Slide 21
Coarse resolution mesh was created using the DEM.
This mesh was created by simply paving elements over the domain.
Vertices: 192 Elements: 334
1000 m
12000 m
12000 m

## Slide 22
High Resolution
Coarse Resolution
Vertices: 6420 Elements: 12742
Vertices: 192 Elements: 334

## Slide 23
Water surface elevations were taken from these vertices

## Slide 24
Coarse No SUB-MESH
Coarse SUB-MESH
High Resolution

## Slide 26
RUN TIMES | 
High Resolution (no sub-mesh) | 591 seconds
Coarse Resolution (no sub-mesh) | 14.5 seconds
Coarse Resolution (sub-mesh) | 20.75 seconds
The sub-mesh adds roughly 40% to computation time.
  This is likely to improve as the code is clean up for use on more realistic test cases.

## Slide 27: Conclusion
The sub-mesh code was able to accurately predict water surface elevation on a coarsened mesh.
The computational cost of the sub-mesh model was close to 30 times less than the high resolution traditional run.
Coarse mesh creation was extremely fast and easy compared to creating the high resolution mesh.

## Slide 28: Future Work
The wetting and drying routine is still being adjusted to allow for smaller .
A threshold of around 5% would be ideal in the future.
The model is also experiencing stability problems at the top of the domain when running multi-day simulations.
Testing on a realistic domain such as Caernarvon Marsh, LA is soon to come.

## Slide 29: Thank you!
Questions?
Thank you to the National Science Foundation for sponsoring this research