INVESTIGATING THE USE OF ACOUSTIC ANGIOGRAPHY AS A TOOL FOR EVALUATING TUMOR RESPONSE TO RADIATION THERAPY

By: Sneha Rao

Honors Thesis

Biomedical Engineering

University of North Carolina At Chapel Hill

April 22, 2014.

Abstract

Acoustic angiography is a novel method that uses a dual frequency ultrasound transducer to image vasculature while eliminating noise from the surrounding tissue7. Given the fact this imaging technique was recently developed, its effectiveness as an imaging technique for clinical applications has not yet been fully verified. Studies have shown that this technique is capable of capturing changes in vascular structure due to tumor angiogenesis7. However, the use of this method in evaluating the efficacy of radiation therapy has not yet been characterized. The purpose of this study was to verify a pilot study that suggested that acoustic angiography was in fact a viable method of evaluating radiation therapy tumor response in a rat model7. To provide additional support for this claim, this study used a rat model with a sample size of seven to assess which metric, tumor size or volume vascularity ratio, were more sensitive to changes in tumor due to radiation. Due to problems with the tumor model and possible tumor necrosis, a clear correlation between the two metrics and diagnostic sensitivity could not be made. While the study was not able to provide conclusive evidence to support the claims made in the previous study, the study did yield insight on better experimental methods and future applicable projects.

Introduction

Due to recent advances in medicine, cancer diagnostics and treatment have changed in a multitude of ways that have significantly improved the quality of life of millions of people. According to recent statistics cited by Cancer Research UK, more than 50% of people diagnosed with cancer live for at least five years after being diagnosed2. Furthermore, the mortality rates for the most common cancers have been on significant decline suggesting that the early diagnosis and new treatment options are effective2.  Early diagnostics efforts are at the forefront of these new, promising trends. While efforts to educate patients about good health practices has played a major role in helping reduce cancer rates, preemptive diagnostic imaging has become one of the main tools for patient diagnostics. In today’s hospitals, patients receive a multitude of imaging procedures to help clinicians determine the diagnoses and potential treatments. The results of various different imaging techniques have become so standardized that physicians will rarely make a significant diagnosis without the help of several scans. Since imaging modalities like magnetic resonance imaging (MRI), positron emission tomography PET, and Ultrasound provide such valuable patient information, major advances in these areas will change the face of medical diagnostics. A study that analyzed over a million inpatient hospitalizations in over 100 hospitals shows that hospitals requiring imaging services for patients had lower mortality than hospitals that do not place emphasis on using imaging as a diagnostic tool10.

In cancer imaging diagnostics, measuring tumor response to therapy is very important in determining the course of care of a patient. Treatment of malignant tumors generally involves therapies that are either invasive or very powerful with adverse side effects. Given these two drawbacks of current treatments, clinicians must be able to accurately discern the effectiveness of treatment so that the patient receives the appropriate level of care. Due to a lack of knowledge about tumor biology, clinicians are unable to determine the exact cocktail of therapies that will benefit a patient without going through several treatment plans. Since there is no perfect algorithm that will help a clinician select a treatment plan, the physician has to use various different metrics to gauge the health of the patient while they are on a particular therapy. Currently, tumor morphology through the RECIST criteria is the standard for measuring tumor response15. While tumor volume can be measured using a variety of different imaging modalities, all the different techniques share some similar drawbacks. One of the major problems with imaging tumors is the fact that the tumor tissue is hard to differentiate from the surrounding tissue. This problem is especially prevalent in anatomical imaging such as ultrasound, PET, and MRI because these diagnostic routines only measure the morphological characteristics of the tumor. And while morphological changes can be a very useful metric for tumor response analysis, there are many instances in which the tumor size remains constant even though it is responding to the treatment5. In such cases, other metrics must be used to determine whether or not the tumor is responding to treatment. Tumors can remain constant in size and experience changes in the internal perfusion or vascular structure. The current RECIST standards only use changes in tumor size to classify changes in tumor response. Using only the tumor morphology to gauge tumor response will be problematic because other criteria such as changes in vascular density might be more sensitive to changes in tumor response7.

Ultrasound and its role as a diagnostic tool

Ultrasound imaging, due to portability, safety and its real time imaging capability make it an excellent diagnostic tool in the clinic. Thanks to recent advances in ultrasound machinery, the use of ultrasound imaging is extending beyond the traditional uses in the diagnostic clinics. A combination of contrast ultrasound and dual frequency imaging has led to the development of a new type of ultrasound modality known as acoustic angiography6.

Developed by the Dayton lab, this new technique makes use of two confocal transducers that are set at different frequencies to transmit and receive the signal6. The transmit-receive coupling mechanism enables this prototype probe to transmit ultrasound waves at a lower frequency of 4 MHz and a high frequency receive signal at 30 MHz6. The concurrent use of both low frequency and high frequency elements enables the transducer to send out lower frequency pulses to stimulate the microbubbles in the vasculature and receive the higher frequency non-linear response form the microbubbles as the signal of interest6. By making use of the non-linear response signal from the microbubbles, the transducer effectively eliminates the background noise from the surrounding tissue and provides a very clean image of the blood vessels.  One of the major benefits of this method of imaging is that it virtually eliminates all the tissue noise that seems to limit the functionality of other imaging modalities6.

Compared to other imaging techniques such as power Doppler sonography, which also has the capability to characterize tumor angiogenesis, acoustic angiography has the added benefit of being able to image micro vessels that are less than 200µm in size6. The increased sensitively of acoustic angiography to the microvascular structure is especially useful in detecting early changes in perfusion at the capillary level, which is one of the early markers for tumor response4.

Obtaining an accurate map of the vasculature can be a very useful diagnostic tool to identify certain diseases and cancers, and to detect the effectiveness of cancer drugs5. At the onset of cancer, the growth of vasculature surrounding cancerous tissue is one of the first indicators of potentially tumorous tissue growth5. When cancer cells begin to grow and divide rapidly they require more nutrients and thus release angiogenic factors to stimulate the growth of nearby vascular networks5. Excess VEGF has been found near areas of tumor metastases indicating that the protein might be a good marker for molecular imaging studies to look for early signs of tumor metastases7.

In this study, tumor volume vascularity is compared against the tumor size to determine which metric is best suited for measuring tumor response to radiation therapy.

Pilot studies using acoustic angiography as the imaging modality to evaluate radiation therapy have demonstrated changes in the density of the vasculature surrounding the tumors that were otherwise undetectable7. The changes in vasculature detected by analysis of tumor vascularity using acoustic angiography preceded any changes based on tumor volume by about 6 days post radiation; therefore indicating that the tumor response in a rat model can be detected much earlier than any morphological response to the radiation therapy7. In order to further verify the results obtained in the pilot study, the following study was conducted with seven rats to discern if tumor vascularity or tumor volume was a better criterion for early detection of tumor response to radiation therapy. The rats were implanted with 9L glioblastoma xenograft tumor cells and allowed to grow until the tumors were palpable and at about 1cm wide. Once the tumors reached a palpable size, seven rats were treated with 20Gy broad beam radiation and imaged every two days with B-mode ultrasound and acoustic angiography. Post-imaging analysis included measuring the dimensions of the tumor using B-mode images and analyzing the volume vascular ratio using acoustic angiograph images.

Materials and Methods

Tumor Model:

Our institutional animal care and use committee (IACUC) approved all animal protocols used in this prospective study. Animals used in this study were seven female Fischer rats obtained from Charles River Laboratories, Durham, NC. Six female rats of about 3 months were anesthetized using isoflurane solution and were then injected subcutaneously in the right hind leg with glioblastoma xenograft tumor cells. After two weeks of inoculation, the tumors were palpable and approximately 1 cm in diameter.

Treatment Protocol

Tumor Injection

The seven rats that were used in the study were separated into the following groups: four rats with tumors that were treated with radiation (treatment group), two rats without tumors that were treated (no tumor group), and one rat with a tumor that was not treated (untreated group). The animals were shaved with an electronic clipper and a debilitating cream was used to ensure that all the remaining hair in the region was removed. A 20-gauge catheter was placed in the tail vein for the administration of contrast material. The contrast agent used was a lipid-encapsulated microbubble solution containing bubbles of about 1 µm diameter. Prior to tail vein injection, the microbubble solution was diluted at a ratio of 1:1 with saline. The microbubble contrast agent was infused with a syringe pump (Harvard Apparatus, Holliston, Mass) at a rate of 40 ul/min.

| Group Name | Treatment | Number of Animals |
| --- | --- | --- |
| Treated | Tumor + radiation | 4 |
| Untreated | Tumor | 1 |
| No tumor | Radiation | 2 |

Table 1: The table shows the treatment groups that were used for the experiment.

Radiation Treatment Protocol

The animals were anesthetized with isoflurane and were shaved and debilitated to clear an area of the rat for treatment. The animal was oriented on the heating pad underneath a linear accelerator. The heating pad is necessary because the animal cannot self-regulate its body temperature. The animal was strapped down to prevent animal breathing respiratory artifact from disturbing the imaging acquisition. The field size was chosen to be 2.5 cm x 2.5 cm and the radiation dose rate was 300mu/min. The animal was treated with the radiation for approximately 7 minutes for a total dosage of 20Gy. All of the treatments were conducted on 2/26/14 at UNC Cancer Hospital Radiology.

Image Acquisition

All images were acquired by Sneha Rao and PhD graduate student, Sunny Kasoji. A VisualSonics Vevo 770 micro-imaging system was used with the adapted dual frequency transducer (adapted from the RMV 707) with a 4-MHz element added confocal outside of the inner 30-MHz element. This enables the transducer to activate the bubbles at the low frequency of 4-MHz and acquire the higher frequency non-linear bubble response while ignoring the lower frequency tissue signal. For each rat that was imaged, a b-mode 3-D scan and a contrast scan was obtained. The transducer probe positioned above the right hind leg and the 3-D motion stage was allowed to move while the 3-D scan was being acquired. This resulted in imaging the entire region where the tumor was implanted.

The images were acquired with a frame rate of 3 Hz and the 3-D smoothing feature was only used for the contrast mode images and not the B-mode images. The imaging began less than 1 minute after the initiation of contrast material infusion and probe was positioned so that it was at the center of the tumor. The distance form the center to either end of the tumor was found to determine the distance to image. A B-mode 3-D scan was acquired prior to injecting the contrast agent and the contrast scan was performed after the microbubbles had been infused for about 15 seconds. After obtaining the scans, the weight of the rat was noted to assess the health of the animal.

Image analysis

Tumor Volume

The tumor volume was calculated using the following equation for an ellipsoid. The dimensions of the tumor were obtained using VisualSonics Vevo software. The height and length measurements were obtained from the tumor cross-section with the largest area. The width of the tumor was determined by measuring the distance between the two ends of the tumor.

Equation used for ellipsoid volume:

(equation 1)

Where V is the volume, a, b and c are the radii of the three axes respectively

Volume Vascularity Ratio

A tumor ROI was isolated on the B-mode image by enabling the user to define the dimensions of the tumor at the largest cross sectional area. Once the ROI was established, it was used to identify the corresponding region in the contrast image. A threshold value was established to distinguish between voxels that represent blood vessels and voxels that represent the surrounding tissue. The following equation was used to calculate a ratio between the vessel voxels and the tissue voxels:

Theoretically the ratio should represent the voxels of blood vessels per total voxel intensity so that one can compare the volume of blood vessels to the total volume of the tumor. This yields a number between 1 and 0, where 1 indicates that the entire tumor volume is filled with perfused vessels and 0 indicates that in the entire tumor volume there are perfused vessels.

The Matlab routine calculated the ratio based on the equation described below;

Volume vascularity ratio:

Results and Discussion

Tumor Volume

After the first day post radiation treatment, the normalized tumor volume of the radiation treated group was calculated to be 1.15 ± 0.64 mm3 and that of the negative control group was found to be 1.4 mm3. The standard deviation of the tumor treatment group is nearly50% of the actual measurement; this indicates that there is a significant amount of variability in the tumor volume measurements in the radiation treated group. The observed variability could be due to variability in tumor growth and inaccuracy when measuring the tumor volume. While the same amount of tumor tissue was implanted in all the rats, they all grew differently in each animal thus leading to the differences in size. The final volume measured at the end of the study, 0.125 mm3 ± 0.093 mm3 has a very low standard deviation indicating that toward the end of the study the tumor volume for the treated rats became very similar. The actual average volume measurement was also the lowest it had been throughout the study indicating that all tumors in the treated group were responding well and decreasing in size. Furthermore, the significant decrease in the standard deviation between the baseline volume and the last data point indicate that not only did the tumors decrease in size overall, they also became more similar in size.

Tumor volume was calculated by approximating the shape of the tumor to be an ellipsoid and then using the length, width, and height of the tumor measurements to calculate a rough volume. Since the tumor cells were injected instead of an intact tumor; the cells could have dispersed from injection site thus resulting in tumors that aggregated together later on in their development. The conjoining of tumors post injection is problematic because the shape of the tumor no longer resembles an ellipsoid and so if an ellipsoid volume was applied over the total area of the combined tumor, we would inadvertently be adding background tissue noise into the volume calculation.

Another limitation was that only one animal that was implanted with a tumor without treatment and thus there were not enough animals in this group to make useful comparisons to the radiated rats. The two rats that were not implanted with tumors did not develop tumors throughout the study and thus no volume data was measured for these two animals. More rats were to be implanted with tumors in order to obtain a larger sample size however the acoustic angiography transducer stopped working and thus more data was not able to be collected. A comparison of the tumor volume of all the animals shows that the general trend for the size of tumor post treatment in the treated group is a decrease in tumor size followed by an increase and then a constant decrease (figure 1). Previous work has exposed that an alternate method of comparison can be used: comparison between tumors that respond to treatment, and tumors that do not, however we are unable to compare our data to such previous work as all rats in this study responded to treatment7. While the treated rats were expected to respond to the treatment, the untreated rat with a tumor had response that was similar to the treated group, which is incongruent with the expected results. Since the untreated rat had no exposure to the radiation or any chemotherapeutic drug the observed decrease in tumor size is most likely due to either an immune response or necrosis. Even though this study did not have the same parameters as the previous pilot study, the trend observed in the treatment group is similar; in both cases there seems to have been a recurrence of the tumor after an initial decrease in tumor volume7. This finding is not expected because radiation therapy is expected to cause a steady decrease in tumor volume. One hypothesis for the unexpected increase in tumor size would be that the radiation might have caused the remaining tissue in the tumor to become more active and rapidly undergo mitosis thereby increasing the tumor size post radiation treatment.

Figure 1. A chart showing the normalized tumor volume of rats in the treatment group (received radiation) and untreated group (no radiation). The major trend observed in the treatment group is that there is a spontaneous increase in tumor size in the middle of the study. Where as in the untreated group the size increases and then decreases back to the baseline value.

Figure 3: The b-mode image on the left is of the tumor in animal 746 (untreated) at time point 3-2 and the b-mode image on the right is of the same animal at the time point 3-13. The image clearly shows the reduction is tumor size between the two time points because the tumor is considerably smaller in size at the second time point.

Volume Vascularity Ratio

Volume vascularity ratio is a measure of the volume of perfused blood vessels in the tumor compared to the total volume of the tumor. A ratio of 1 would indicate that there is no tissue and only perfused blood vessels in the region of interest encircled around the tumor. Similarly a ratio of 0 would indicate that there are no blood vessels present in the area in the tumor. The graph below of the volume vascularity ratio for each animal is very low for all time points and does not seem to show any conclusive trends or results. The lack of trends is mainly due to the fact that the threshold ratio value that was chosen to separate the intensity of a blood vessel and surrounding tissue was too high. This would result in all of the lower intensity voxels that belong to vessels being characterized as surrounding tissue. Based on previous data collected in a pilot study one would predict that for the treatment group, the vascularity ratio to increase with time and then the decrease significantly from the untreated group7.  Since the untreated group does not have any contact with the radiation therapy, one would predict that the vascularity of the tumor, as defined by the vascularity ratio, would remain unchanged. For the treated group, one would hypothesize that the ratio decreases consistently because the radiation down regulates angiogenic pathways in the endothelial cells of the tumor9. The inhibition of angiogenesis in the tumor EC will affect the surrounding vascular network by decreasing the concentration of angiogenic factors, which would decrease blood vessel growth9. However conflicting evidence has also suggested that low doses of ionizing radiation enhance angiogenesis in tumors and actually promote tumor growth12. Given such contrasting results, the role of radiation on vascularity around tumors is not yet fully understood.

Figure 2. The chart above shows the volumetric vascular ratio compared to time through the experiment. Since the value of the ratio is very low, it is hypothesized that the threshold that was chosen for the analysis was too high and thus skewed the data.

Figure 4: The acoustic angiography image on the left is of the tumor in animal 746 at time point 3-2 and the image on the right is of the same animal at time point 3-13. The main difference between the two images is that there seems to be higher vascularity in the second image.

Conclusions

For the untreated rat, we expected the tumor volume to increase steadily with time because there was no anticancer treatment delivered to the rat; however we observed a contradictory trend. The volume initially increased until 3-2-14. However, after that point the volume continually decreased back to its original size. One possible explanation for this observation is that the tumor may have become necrotic and stopped growing at time point 3-2-14. Once the tumor became necrotic it could no longer proliferate and the cancer cells underwent premature death due to lack of nutrients14. The early necrosis of this tumor might be due to the fact that this tumor model experienced very rapid growth. Using a tumor model that has a slower growth rate might ameliorate the issue of pre-mature tumor necrosis. In the future histological data will be obtained in order to verify that tumor necrosis occurred.

The tumor volume results for the treatment group were also somewhat unexpected because the normalized tumor for the group of four rats increased post radiation until about 3-6-14, after which the size steadily decreased past the baseline value. An interesting finding for this data set is that the tumor volume increased before it began decreasing, this trend was also observed in previous studies7. One possible explanation for this biphasic trend is that the broad beam radiation stimulated the endothelial cells adjacent to the tumor to release growth factors that were taken up by the tumor. Based on a recent studied that suggested that ionizing radiation can stimulate angiogenesis in non-cancerous endothelial cells we would hypothesize that perhaps this mechanism is the underlying cause of the unexpected growth in tumor size for the treated tumor bearing rats13. Furthermore the sample size was again an issue in this analysis as well. Conclusive statements about the observed trends cannot be made on such a small data set.

One of the underlying purposes of this study was to gauge whether or not the tumor model derived from the University of Virginia, the 9L glioblastoma xenograft tumor cells, were a viable option for acoustic angiography studies. Based on the results of this study and the complications that were faced, this tumor model does not appear to be stable enough for these studies. One of the biggest complications that were experienced was that the tumors grew very quickly and thus the imaging time-line was too infrequent to capture precise changes in the tumor size and vascularity. Furthermore, once the tumors were of palpable size, it was observed that the tumor shape was not uniform on the animal. Some animals, namely, 746, had two tumors that coalesced into one and made it difficult to obtain an accurate tumor volume and volume vascularity ratio measurement. Conversely the tumor in animal 873 became so flat that it had to be removed from the data set because it was an outlier. In future studies, one would utilize tumor models that are known to deliver stable tumors that are uniform in shape so that the error in tumor volume calculation can be minimized. Also to further increase the resolution of our data set, we will image the animals at small intervals so that we can detect more minute changes in the size and vascularity of the tumor.

While this study did not provide ample support necessary to verify the finding that acoustic angiography can be a useful diagnostic technique to measure tumor response in radiation therapy, the study did elucidate some inherent complications of the experiment and provided support for changes in experimental procedure for future studies. Repeating this study with a slower growing tumor model could potentially eliminate many of the complications with tumor shape that were observed in this study. Future studies in the effects of radiation on the vascular structure of tumors may help explain some of the unexpected observations that were observed in this study. Given molecular biology research that suggests that ionizing radiation promotes angiogenesis in non-tumor bearing tissue and inhibits angiogenesis in tumor bearing tissue, a potential application for acoustic angiography might attempt to quantify the structural differences between radiated tumor vasculature and radiated non-tumor bearing vasculature12. The present study attempted to do such a comparison by measuring vascular density in a tumor. However, examining the structural differences with vessel segmentation analysis might yield more indicative results as to how the radiation affects vascular structure5. To study the effect of radiation on vascular function, future experiments should use Doppler imaging to analyze the change in flow.

Next Steps

While the results from the study did not address the use of acoustic angiography as a diagnostic tool to assess radiation, they did shed light on better experimental techniques and further studies. Some experimental techniques that would greatly benefit a future study would be utilize a more well characterized tumor model, increase the number of imaging time points, eliminate artifacts that would otherwise impede quality of ultrasound image, and include a larger sample size (N>7). In addition, the vascular structure surrounding tumors could be further characterized through quantitative means such as vessel segmentation analysis. Since studies have already established that changes in the vascular structure can be used as a metric to analyze tumor response due to anti-angiogenic drugs, applying the same quantitative method of vessel analysis to tumors treated with radiation could yield promising results. It would also be very pertinent to investigate the effects of different types of radiation and intensity of radiation on the efficacy of acoustic angiography as a diagnostic imaging modality. Furthermore given the biphasic nature of the data and recent evidence that radiation can cause angiogenesis given certain conditions, it might be useful to study blood vessel growth using acoustic angiography to analyze vascular structure and molecular imaging to analyze change in angiogenic factors. Given the importance of the vascular network in body and its sensitivity to various different conditions, using acoustic angiography to map and analyze vascular structure might be the next big step in medical imaging.

Works Cited

- "Comparing Different Types of Imaging." Medical Imaging Comparison. N.p., 23 May 2013. Web. 23 Apr. 2014.

- "Surveillance, Epidemiology, and End Results ProgramTurning Cancer Data Into Discovery." Cancer of All Sites. N.p., n.d. Web. 23 Apr. 2014.

- Bullitt E, Muller KE, Jung I, Lin W, Aylward S. Analyzing attributes of vessel populations. Med Image Anal. 2005;9(1):39-49.

- Gessner R, Lukacs M, Lee M, Cherin E, Foster FS, Dayton PA. High-resolution, high-contrast ultrasound imaging using a prototype dual-frequency transducer: in vitro and in vivo studies. IEEE Trans Ultrason Ferroelectr Freq Control. 2010;57(8):1772-81.

- Gessner RC, Aylward SR, Dayton PA. Mapping microvasculature with acoustic angiography yields quantifiable differences between healthy and tumor-bearing tissue volumes in a rodent model. Radiology. 2012;264(3):733-40.

- Gessner RC, Frederick CB, Foster FS, Dayton PA. Acoustic angiography: a new imaging modality for assessing microvasculature architecture. Int J Biomed Imaging. 2013;2013:936593.

- Gessner, Ryan. "Acoustic Angiography: A New Imaging Platform for High Resolution Mapping of Microvasculature and Tumor Assessment." Diss. U of North Carolina at Chapel Hill, 2013. Print.

- Grabham P, Sharma P, Bigelow A, Geard C. Distinct mechanisms of the inhibition of vasculogenesis by different species of ionizing particles. J Radiat Res. 2014;55 Suppl 1:i44-i45.

- Grabham, Peter, and Preety Sharma. "The Effects of Radiation on Angiogenesis." Vascular Cell 5.1 (2013): 19. Vascular Cell. 26 Oct. 2013. Web. 23 Apr. 2014.

- Lee DW, Foster DA. The association between hospital outcomes and diagnostic imaging: early findings. J Am Coll Radiol. 2009;6(11):780-5.

- Nishida N, Yano H, Nishida T, Kamura T, Kojiro M. Angiogenesis in cancer. Vasc Health Risk Manag. 2006;2(3):213-9.

- Oh ET, Park MT, Song MJ, et al. Radiation-induced angiogenic signaling pathway in endothelial cells obtained from normal and cancer tissue of human breast. Oncogene. 2014;33(10):1229-38.

- Sirsi SR, Flexman ML, Vlachos F, Huang J, Hernandez SL, Kim HK, Johung TB, Gander JW, Reichstein AR, Lampl BS, Wang A, Hielscher AH, Kandel JJ, Yamashiro DJ, Borden MA. “Contrast ultrasound imaging for identification of early responder tumor models to anti-angiogenic therapy,” Ultrasound Med Biol. 2012 Jun;38(6):1019-29. doi: 10.1016/j.ultrasmedbio.2012.01.014. Epub 2012 Mar 16.

- Weber WA. Assessing tumor response to therapy. J Nucl Med. 2009;50 Suppl 1(Suppl_1):1S-10S.

- "Cancer Imaging Program." Imaging Response Criteria. National Cancer Institute, n.d. Web. 23 Apr. 2014.

Diagnostics or diagnostic?

Define term

You could mention RECIST here.  That is the term for what you are referring to – google it.

Assessing vascularity is not molecular imaging.

Molecular imaging with ultrasound is not used clinically yet.  MRI not so much either.  Really, PET is the only clinical used molecular imaging tool right now.

Well, actually PET pretty universally uses one marker - FDG – glucose uptake – in tumors for screening, so this sentence is not very accurate.

A tumor wouldn’t “respond” to molecular markers, it would “express” molecular markers.

Sneha, you spend a lot of time talking about why molecular imaging is not a great alternative.  I wouldn’t really spend so much effort.  The reason is because molecular imaging is in fact really very new, and is just not used with any modality clinically except PET.  And, there is preclinical data that it may actually work fairly well for indicating tumor response.   So, your argument should be that tumor size (RECIST) is probably not a good marker of tumor response, and don’t talk much about molecular imaging because we just don’t really know yet if it will work well or not clinically.

Portability and safety (does not use ionizing radiation like CT and PET) also very important

Less than 200 microns.  Probably not possible to image vessels below 100 mcrons.

You should include an “abbreviations” section…most likely required by the university formatting guide…

Wait, isn’t this the second of the aforementioned three? If not, then you should clarify.

Plural, thus “have” instead of “has”

In what subjects? Rats? Humans? Mice? Cells? Stuffed animals?

Again, this should go in a table of abbreviations.

Aw! I used Charles River for my Ph.D. work …different type of rat though…double check this with Sunchip or Daytona heights.

“depilating” – means removing hair!  Not debilitating!

Was is? Huh?

Hooray for equation editor…

Perfused?

Is are you reporting variance above or std dev?

Might consider moving this to “Discussion”

Compare this std to previous.

Discussion material.

Yes, this is a big point with your study.  The sample size was not big enough to do much.  You need to talk about why that was.  It would not be a good scientific practice to start a study that was doomed to fail because there was not enough animals to start with!

I think there are 2 potential explanations.  1) you intended to use more animals but the tumors did not take in some and 2) this experiment was intended to be repeated with multiple groups to increase N but because of the broken transducer you only had time to study 1 group.

p.s. check your font size, seems like there may be different font sizes.

Nice thinking for a hypothesis, but I don’t think this is right.

I also wouldn’t use the term “ablate” here – which usually means to heat tissue until it kills tissue.  Radiation does not kill tissue by heating in this case.

What usually happens (and seems to be shown in Figure 1), is that the radiation causes cell death in the tumor, which reduces growth and size, but then the remaining cells in the tumor that were not killed grow aggressively and then the tumor recovers after a short period of regression.  This is a nasty thing – the radiation knocks it out for a short time, but then it comes back!

What doesn’t make sense is why all the tumors die out again a few days later.  We would expect them all to keep growing.  I think that is due to a problem with this tumor model.  You can say that this is a new model for our group and this growth pattern was unexpected.

WHERE is your caption girl?! Fix that!

NO PRONOUNS!

WTF PRONOUNS! “One may infer/hypothesize…etc.”or “an inference can be made” or “a hypothesis can be made”

Citation!!!

GIRL! Where is your CAPTION!

So, why didn’t you analyze the data again with a different threshold?

That is probably true – but it is also surprising the volume shrank so quickly! We don’t know why this was.  I wouldn’t have expected it

You should mention that histology should have been conducted to determine whether this was necrotic indeed.

Previous work.

That’s probably true.  Note that as I said earlier, it knocks out some of the tumor – but then the tumor comes back

Where was that stated?! You should state this at the beginning…

You should avoid using negative words like “not” where possible…use the negative of a word instead of putting “not” in front of it…

(see prior comment about explaining why the sample size was so small – it shouldn’t have been if the experiments were all done as originally planned)

For significance, you should also mention that a larger number of animals should be included in the study.

Citation?